## Slide 1
Urban Air Quality
Early Warning System
Mid-semester project progress
PM2.5 and PM10 daily forecasting in Delhi
Submitted to Prof. Anupam Singhal
Prepared by [student / team names] | 9 October 2026
Notes: Introduce the research question: can a model improve on carrying forward yesterday's PM? This is a prototype, not an official health alert.

## Slide 2
Research question and project status
02
Can weather, prior PM and calendar effects beat persistence?
Completed
Two-pollutant acquisition and caching
Audited station archive merge
Chronological backtests and live dashboard
Next stage
Prospective forecast versus later actuals
Fixed issue-time weather validation
Longer station and fire coverage
Notes: The prototype and historical evaluations are implemented. Prospective live accuracy remains work in progress. Do not call the system complete or clinically validated.

## Slide 3
Two distinct targets, uneven five-year coverage
Five years is the calendar window. Valid daily targets are fewer.
03
Target | Calendar span | Valid days
CAMS modeled PM2.5 | 9 Oct 2021 - 8 Oct 2026 | 1,526 / 1,826
CAMS modeled PM10 | 9 Oct 2021 - 8 Oct 2026 | 1,526 / 1,826
R.K. Puram PM2.5 | 6 Oct 2021 - 5 Oct 2026 | 1,610 / 1,826
R.K. Puram PM10 | 6 Oct 2021 - 5 Oct 2026 | 1,594 / 1,826
CAMS is modeled atmospheric output. R.K. Puram is a station observation series.
Notes: Open-Meteo CAMS global history starts in August 2022. Station observations are from CPCB CAAQM via XKDR and OpenAQ. Missing particulate targets are not imputed. Sources: https://open-meteo.com/en/docs/air-quality-api ; https://airquality.xkdr.org/ ; https://docs.openaq.org/aws/about

## Slide 4
Station sources pass the overlap gate
Matched local hours from XKDR and OpenAQ, February to September 2025
04
6,167
matched hours
95%
preset agreement gate
Matched readings within 1 ug/m3 (%)
Chart: 
| PM2.5 | PM10
Within 1 ug/m3 | 98.9 | 97.7
Median signed difference: 0.0 ug/m3 for both pollutants.
Notes: Our gate required at least 95% of matched hourly readings within 1 ug/m3 and median signed difference no greater than 1 ug/m3. PM2.5 achieved 98.9%; PM10 97.7%. Unmatched hours remain. OpenAQ unit strings contain replacement characters, so byte-level unit equality was not verifiable. See results.json source_audit.

## Slide 5
Date-aware features and simple comparators
05
Weather
Temperature, humidity, wind, rain, pressure, cloud cover, gusts and boundary-layer height
Pollution history
Exact calendar-day lags 1, 2, 3 and 7; complete prior seven-day mean
Calendar
Season, weekend, Indian public holidays and Diwali proximity
Persistence | Seven-day mean | Climatology | Ridge | Random Forest
Satellite fire detections are optional research data; they are not in this five-year model.
Notes: The shared model has 21 inputs. All rolling PM features are shifted before the target date. Weather imputation and Isolation Forest are fitted only on training dates. If anomaly filtering leaves fewer than 10 normal rows, fitting falls back to all usable training rows. Calendar signals are activity proxies, not measured traffic.

## Slide 6
The latest 180 days stay out of model fitting
06
1
Earlier seasonal windows
Select a method using chronological holdouts.
2
Final 180 calendar days
Score every method on the same available dates.
3
Recursive seven-day outlook
Future lags use prior predictions, not future actual PM.
Notes: No random train/test shuffle. Preprocessing and fit use training rows only. Each one-day test prediction may use the true previous-day PM. The final test uses stitched historical-forecast weather, not one archived forecast frozen before each target date. Human development did inspect final metrics, so this is not a pristine blind trial. Source: https://open-meteo.com/en/docs/historical-forecast-api

## Slide 7
Station PM10 improves, other targets keep persistence
Final chronological test; MAE in ug/m3, lower is better
07
Target | Scored | Selected | Selected MAE | Persistence MAE
CAMS PM2.5 | 180 / 180 | Persistence | 16.62 | 16.62
CAMS PM10 | 180 / 180 | Persistence | 86.99 | 86.99
Station PM2.5 | 131 / 180 | Persistence | 12.12 | 12.12
Station PM10 | 133 / 180 | Random Forest | 27.61 | 37.41
26.2%
station PM10 MAE reduction versus persistence
Notes: Station PM10 Random Forest achieved R2 0.732, exceedance recall 92.3%, precision 88.4%, false-positive rate 26.2% and exceedance base rate 68.4%. Station PM2.5 Random Forest scored 11.52 on the final test versus persistence 12.12, but won only 7/10 earlier windows; the rule required 8/10, so it was not promoted. Do not compare raw PM2.5 and PM10 MAEs across concentration scales. Internal evidence: results.json saved 9 October 2026.

## Slide 8
The forecast exposes observation latency
A saved 9 October station PM10 example; live values will refresh
08
Daily PM10 prediction (ug/m3)
Chart: 
| 10-10 | 10-11 | 10-12 | 10-13 | 10-14 | 10-15 | 10-16
Station PM10 modeled outlook | 168 | 142.9 | 132.7 | 172.7 | 189.7 | 185.5 | 158.8
5 to 11
effective lead days
Station cutoff: 5 Oct
Display: 10-16 Oct
If the station is more than five days old, the app switches to a CAMS outlook.
Notes: The saved forecast is a dated example, not a promise for the presentation day. The app internally bridges missing days. At issuance on 9 October, the first displayed station date 10 October has effective lead 5, not 1. If the station grows more than five days stale, CAMS becomes the outlook. It is not an official health alert.

## Slide 9
What the mid-semester result does not establish
09
Current limits
CAMS is modeled, not field truth
Station test loses dates to missingness
Historical weather is not fixed issue-time input
No mature prospective live evaluation
Next work
Log immutable forecasts before outcomes
Score later against station actuals
Test fixed issue-time weather forecasts
Expand and audit external signals
The honest finding: model complexity helps observed PM10 here, but not consistently elsewhere.
Notes: The latest 180 days are excluded from fitting and programmatic model selection, but were inspected during project development. Do not claim a one-time blind test. Prospective accuracy needs forecasts timestamped before their targets and matched to later outcomes. CPCB 24-hour standards: PM2.5 60 ug/m3, PM10 100 ug/m3. Source: https://cpcb.gov.in/upload/NAAQS_2019.pdf